## Slide 1: Running Live Sound
Ryan Gardner
ryangardner@dadeschools.net

## Slide 2: Cable Management
XLR Cables – around $10-$15 for a 25-foot cable
  Mostly used for speakers and microphones
¼” Cables – around $10-$15 for a 25-foot cable
  Mostly used for guitars and amplifiers, can be used as an insert for some wireless microphone systems and for monitors/speakers.
Speak-On Cables – around $25-$30 for a 50-foot cable
  Used to plug in certain speakers to a mixer
¼ Inch XLR Speak-On

## Slide 3: Basic Miscellaneous Cables/Adapters
3.5mm Stereo Male to Male RCA (Used for plugging in audio devices such as IPAD, CD Player, etc.)
¼” male to 1/8” female adapter

## Slide 4: Basic Miscellaneous Cables/Adapters (contd.)
¼” male to XLR Male/Female
iPhone lightning cable to 3.5mm

## Slide 5: Cable Management (Contd.)

## Slide 6: Dynamic Microphones
Dynamic Microphones
  Best for: Powerful (direct) Vocals, capturing strong/loud sounds
  Set-up: Close proximity to sound source
  Common makes+models
    Industry standard: Shure SM57 and Shure SM58
    Cheaper Alternatives: Shure PG58-XLR, Sennheiser E835, AKG D5

## Slide 7: Condenser Microphones
Require 48v power from sound board (phantom power)
Pencil Condenser Mic (Usually sold in pairs):
  Best for: Large group ensembles (vocal or instrumental), drum overheads
  Industry standard: Rode NT5
  Affordable alternatives: AKG P170, Samson C02PR, Rode M5-MP
Large-Diaphragm Condenser Mic
  Best for: vocals/spoken word, solo instrument
  Options: MXL 2003a, Blue Spark, Rode NT1-A, Blue Bluebird

## Slide 8: Miscellaneous/Specialized Mics
Supercardioid Dynamic Kick Microphone (Drum Set Bass Drum)
  Options: Shure BETA 52A, Audix D6, Sennheiser e602 II
Boundary Microphone (Most commonly used for pianos; also can be used to pick up room sound
  Options: Audio-Technica Pro 44, Audix ADX60, Shure MX391
Headset Microphones (Solo vocals/speaking with movement) ***Unless you want to be restricted by the wires, be sure it comes with or is compatible with a wireless body pack.***
  Options: Shure SM31FH, Audio-Technica ATW1101H92 System10 Pro92cW

## Slide 9: Wireless Microphones
Has a wireless receiver that needs to be plugged into the sound mixer (usually XLR cable but can also be ¼” cable)
Microphone and receiver need to be set to the same frequency band
Wireless receiver has it’s own independent volume knob
Microphone is battery operated

## Slide 10: Sound Mixers Basics
Unpowered mixers need powered speakers
Powered mixers need unpowered speakers
Make sure board includes phantom power (48v)
Check cable output type on mixers to make sure your mixer will be compatible with your speakers

## Slide 11: Sound Mixers
Powered Sound Mixer:
  Usually heavier due to built-in amps, better for permanent performance locations
  Requires unpowered speakers
  system usually stays connected to speakers and just has to be turned on to be performance ready.
Unpowered Sound Mixer:
  Usually lightweight, good for on-the-go performances
  Require an external amplifier or powered speakers (need a power cable to turn on the speakers).
  Includes more features and effects

## Slide 12: Powered Speakers (a.k.a. active speakers)
Requires a power chord to be plugged in
Has separate volume control from mixer
Usually connects to mixer with XLR or ¼” cables
Works with unpowered mixers

## Slide 13: Unpowered Speakers (a.k.a. passive speakers)
Usually connects to mixer with speak-on or ¼” Cables
Does not require a power chord to plug in
Does not have a separate volume control from the mixer
Works with powered mixers

## Slide 14: Powered Mixer/ Unpowered Speakers Options
Powered Mixers:
  Yamaha EMX5016CF
  Behringer Europower PMP2000D
  Behringer Europower PMP1680S
Unpowered Speakers:
  JBL JRX215
  Yamaha CBR15
  Mackie Passive Speaker, 600W (C300z)

## Slide 15: Unpowered Mixer/Powered Speakers Options
Unpowered Mixers:
  Mackie ProFXv2
  Behringer Xenyx X1222
  Soundcraft EPM Mixer
Powered Speakers:
  Mackie Thump12A
  Rockville RPG15
  Behringer Eurolive B210D

## Slide 16: The Anatomy of a Sound Board
Channels
Outputs
Gain
EQ
Mute/Solo
Speaker Assign

## Slide 18: Let’s Talk Channels!
Each Microphone is controlled by a column of controls called a “channel”
  The controls for the channels usually include:
    Mic input
    Line-in/Insert
    Mic Gain
    EQ
    Aux/Fx (Sometimes)
    Pan
    Mute
    Volume Slider

## Slide 19: Gain Vs. Volume
Gain: The strength of a signal being inputted into the mixer
  The more the gain, the more strength of tone
  No processing on the signal yet
Volume: The amount of sound (in dB) that is being outputted to the speakers. This signal is sent out after the signal has been processed.
  If you have low gain, and high volume, the overall tone of the outputted signal will be very flat/lacking in tone.

## Slide 20: Inserts/Line-ins
XLR Female Port
Line/Hi-Z Button
  Hi-Z button rarely used for microphones, mostly used for guitar
Line/Hi-Z In 1
  Used to connect something that does not have an XLR option (i.e a guitar, a wireless microphone receiver, etc.)
Insert
  For our purposes, this will rarely be used.
  Mainly used to add in some type of external effects processor

## Slide 21: Gain and EQ
The gain knob controls how much signal you want to send into your board before it is processed.
  Usually, the higher the gain, the better tone you will get out of your equipment
Equalizers (Eqs)
  Controls which frequency of sounds you want to boost or reduce.
    LOW EQ: Controls low sounds (plosive consonants, proximity effect, etc.)
    MID: Usually the warm part of the speaking voice
    High: Usually the higher frequency consonants of the speaking voice (like s)

## Slide 22: AUX, FX, and Pan
AUX: Used in conjunction with Fx knob.
  Taps off channel’s signal so you can send it to an Aux Bus.
Fx knob: controls how much signal has an effect added to it
Pan: Allows you to focus specific instruments to come out of a specific speaker (Left to Right). Changes directionality of sound being outputted.

## Slide 23: Mute Button and Volume Slider
Mute Button
  Not a global mute
  Mute’s only the channel on which it lies
Volume Slider
  Controls the amount of signal that goes out through the speakers

## Slide 24: Stereo Graphic EQ
Can be used for a more focused overall control on low/mid/high frequencies
  I normally control my EQs on the individual channels. The only time I use the stereo graphic EQ is when I am playing music through the sound board
  Safe to set each frequency range to the middle (0)

## Slide 25: Phantom Power
Usually found either next to the main meters or as a smaller switch in the back of the board next to the power switch
  If this is not on, condenser microphones will not work

## Slide 26: Fx Control
Used to add effects, mainly reverb, onto vocal microphones
  Effect can be directed to specific channels using the Fx knob on each individual channel
  Different types of reverbs can be selected by turning the preset knob to the number desired
Fx to master
  Sends signal with effects to the slide control for the speakers
Fx to monitor
  Sends signal with added effects to the slide control for the monitors

## Slide 27: Master Volume
Main
  Controls the amount of signal that is sent to the speakers that are plugged into the “main out” ports
Mon
  Controls the amount of signal that is sent out to the monitors that are plugged into the “monitor out” ports

## Slide 28: Mic-ing a Large Ensemble

## Slide 29: Mic Stands
Tripod Boom Stand
  Good for mic-ing individual acoustic instruments
  Better overall mobility for Mic placement

## Slide 30: Mic Stands
Round-Base Stand
  More sturdy
  Less Flexibility in terms of mic placement

## Slide 31: Mic Stands
Short Tripod Boom Stand
  Good for mic-ing seated instruments without obstructing view of performer
  Less Bulky
  Good flexibility in terms of mic placement

## Slide 32: Feedback
Some techniques for controlling feedback:
  The speakers should be facing out towards the audience and should be in front of the stage
  Microphones should remain behind the speakers
  General volume adjust with gain knob during sound checks
    After, adjust levels for sliders
  Mute any unused microphones/channels
  It is better to add volume for all channels by using the main output slider than raising each individual channel/microphone

## Slide 33: Set Up!
Step 1: Set speakers up in the location you want them
Step 2: Connect Mixer to Power Source
Step 3 (Optional): If using an unpowered mixer, connect speakers to power source
Step 4: Connect speakers to “Main Out” (L/R) ports on sound board (either XLR, ¼” cables, or speak-on cable depending on board)
Step 5: Turn on sound mixer
Step 6 (optional): Turn on powered speakers
Step 7: Connect Microphones/Instruments to board inputs
Step 8: Adjust levels (turn up slider for main out, adjust levels on each channel)

## Slide 34: I’m Set-Up but No Sound is Coming Out!
Checklist:
  Are the mixer/speakers plugged in and turned on?
    If they are plugged in to a power strip, is the power strip switched on?
  Is everything plugged into the right spot?
  Have I turned up the sliders on my outputs?
  Have I assigned the channels I am using to a speaker?
  Is the Channel Mute on?
  Do I have a channel solo button selected on a different channel?
  Is the gain and/or volume slider turned up on the channel I am using?
  Does the microphone have a power switch? Is it turned on?
  If I am using a condenser microphone, is phantom power turned on, on the sound board?
  If I am using powered speakers, is the volume turned off on the back?

## Slide 35: Troubleshooting Checklist
If you have completed the previous checklist, and are still not getting any sound, it’s time to troubleshoot!
  Try a different channel on your sound board
  Try using a different microphone
  Try using a different Cable
  If you are using a wireless microphone, make sure it is on the same band as the receiver
  Check the signal indicator to see if any signal is being sent to the speakers

## Slide 36: Miscellaneous Equipment
Snake
  The “XLR Extension Chord”
    Necessary for situations where the sound board is far away from the stage
DI Box
  Used as a “splitter” which allows you to connect a guitar to both the amp (which will act as a monitor for the performer) and the sound board so you can adjust the amount of signal of the guitar being sent into the mix.
    Works with bass guitar, keyboards, anything that uses a ¼” connection

## Slide 37: Complete Starter Setup
Mackie ProFX8v2 Unpowered Mixer- $219.00
Rockville RPG122K Powered Speakers - $229.95
4 x 25’ XLR Cables - $40-$50
2 x 50’ XLR Cables - $30-$40
4 x microphone stands - $80 - $120
2 x Shure PGA58 vocal microphones - $108
1 x Samson C02PR stereo pair (2 mics) pencil condenser mic - $106
2 x 25” ¼” cables - $30
_____________________________________________________________________
Total: $843 - $903
This estimate is based on retail values. It does not take into account your school’s tax-exempt status and education discounts.